## Slide 1
STATIC ROUTING & PING
SIMULATION
Computer and Network Communications
Cisco Packet Tracer Analysis
PC
SWITCH
ROUTER
ROUTER
PC
Prepared from the supplied Packet Tracer topology diagram
Computer and Network Communications | Static Routing & ICMP Ping 1

## Slide 2
1. Objectives and Assignment Requirements
• Build and test the two network topologies in Cisco Packet Tracer.
• Configure IP addresses and default gateways according to the labels in the supplied diagram.
• Use ICMP Ping to test communication between selected host IP addresses.
• Explain packet forwarding, routing-table lookup, and the return path.
• Analyze successful and failed ping results using Packet Tracer Simulation Mode.
Important topology check
The assignment text says each topology should contain 5 computers. In the supplied screenshot, each illustrated topology visibly shows 4 PCs. Add a fifth PC to each topology if the instructor requires exactly 5; use an unused IP in the correct subnet.
Computer and Network Communications | Static Routing & ICMP Ping 2

## Slide 3
2. Supplied Packet Tracer Topologies
The screenshot below is included as the reference design provided for this presentation.
Computer and Network Communications | Static Routing & ICMP Ping 3

## Slide 4
3. Topology 1 — One Router, Two LANs
What the diagram shows
• One 2901 router connects two separate IP networks through two interfaces.
• Left LAN: 192.168.1.0/24; router gateway shown as 192.168.1.1.
• Right LAN: 192.168.2.0/24; router gateway shown as 192.168.2.1.
• Switches provide Layer 2 connectivity between the router and PCs.
IP addressing from the screenshot
Device | IPv4 address | Default gateway
Router LAN 1 | 192.168.1.1 | 192.168.1.1
PC0(1) | 192.168.1.100 | 192.168.1.1
PC1(1) | 192.168.1.200 | 192.168.1.1
Router LAN 2 | 192.168.2.1 | 192.168.2.1
PC2(1) | 192.168.2.100 | 192.168.2.1
PC3(1) | 192.168.2.200 | 192.168.2.1
Routing note: both LANs are directly connected to the same router. No static route is needed between these two directly connected networks when both interfaces are up.
Computer and Network Communications | Static Routing & ICMP Ping 4

## Slide 5
4. Topology 2 — Two Routers and Three IP Networks
• R0 connects the 192.168.1.0/24 LAN to the inter-router link.
• R1 connects the inter-router link to the 192.168.3.0/24 LAN.
• The inter-router network uses 192.168.2.1 and 192.168.2.2 as shown.
• Each PC must use the router interface on its own LAN as its default gateway.
Device / interface | IPv4 address | Subnet mask
R0 — left LAN | 192.168.1.1 | 255.255.255.0
R0 — link to R1 | 192.168.2.1 | 255.255.255.0*
R1 — link to R0 | 192.168.2.2 | 255.255.255.0*
R1 — right LAN | 192.168.3.1 | 255.255.255.0
PC0 | 192.168.1.100 | 255.255.255.0
PC1 | 192.168.1.200 | 255.255.255.0
PC2 | 192.168.3.100 | 255.255.255.0
PC3 | 192.168.3.200 | 255.255.255.0
*The screenshot labels only the IP addresses, not the masks. This deck assumes /24 (255.255.255.0) for the 192.168.2.x inter-router link to match the visible addressing. A /30 point-to-point subnet is also common, but would require changing the link addresses/masks consistently.
Computer and Network Communications | Static Routing & ICMP Ping 5

## Slide 6
5. Static Routes for Topology 2
Why static routes are required
• R0 knows its directly connected 192.168.1.0/24 and 192.168.2.0/24 networks, but it does not automatically know the remote 192.168.3.0/24 LAN.
• R1 similarly needs a route back to 192.168.1.0/24. A ping needs a forward path and a return path.
On R0
enable
configure terminal
ip route 192.168.3.0 255.255.255.0 192.168.2.2
end
On R1
enable
configure terminal
ip route 192.168.1.0 255.255.255.0 192.168.2.1
end
Verify routes with: show ip route | Expected static-route code: S
Computer and Network Communications | Static Routing & ICMP Ping 6

## Slide 7
6. Configuration Workflow in Cisco Packet Tracer
1
Place devices
Add 2901 routers, 2960 switches, and PCs; connect using appropriate copper Ethernet cables.
2
Configure router interfaces
Use CLI or Config tab to assign the labelled IP addresses, then issue no shutdown on each used interface.
3
Configure PCs
Desktop → IP Configuration: enter each PC IP, subnet mask, and the local router interface as Default Gateway.
4
Add static routes
For the two-router topology, add the routes shown on the previous slide on both routers.
5
Check interfaces
Use show ip interface brief; used interfaces should be up/up.
6
Test connectivity
Ping the local gateway first, then a remote PC. Use Simulation Mode to inspect the ICMP packets.
Computer and Network Communications | Static Routing & ICMP Ping 7

## Slide 8
7. What Happens During a Ping?
Example: PC0 (192.168.1.100) pings PC2 (192.168.3.100) in Topology 2
1. PC creates ICMP Echo Request
The source checks whether the destination is in its local subnet. 192.168.3.100 is remote.
2. PC sends to its default gateway
PC0 resolves the gateway's MAC address using ARP, if it is not already cached.
3. R0 forwards the packet
R0 checks its routing table and matches the static route to 192.168.3.0/24 via 192.168.2.2.
4. R1 delivers to the destination LAN
R1 sees 192.168.3.0/24 is directly connected, resolves the destination MAC if needed, and forwards the frame.
5. PC2 sends an Echo Reply
The reply travels back through R1 and R0; the return static route on R1 is essential.
ICMP Echo Request = type 8; ICMP Echo Reply = type 0 (IPv4).
Computer and Network Communications | Static Routing & ICMP Ping 8

## Slide 9
8. Observe the Packet in Simulation Mode
• Switch from Realtime to Simulation in Packet Tracer.
• Use Add Simple PDU (envelope icon) or run ping from a PC command prompt.
• Use Capture/Forward to move the event one step at a time.
• Open each event to inspect OSI layers, source/destination IPs, and ICMP type.
• Expect ARP events before the first ICMP exchange when MAC addresses are unknown.
• A green check or successful ping indicates replies were received; red events/timeouts require troubleshooting.
PC0
R0
R1
PC2
Request: PC0 → PC2
Reply: PC2 → PC0
Remember: the Ethernet source/destination MAC addresses change at each routed hop. The source/destination IP addresses normally remain the same end-to-end (unless NAT is used).
Computer and Network Communications | Static Routing & ICMP Ping 9

## Slide 10
9. Suggested Ping Test Matrix
Record actual results from your own Packet Tracer file; do not claim success until tested.
Topology | Source | Destination | Expected result | Reason
1 | 192.168.1.100 | 192.168.1.200 | Success | Same LAN / subnet
1 | 192.168.1.100 | 192.168.2.100 | Success | Router has both LANs directly connected
1 | 192.168.2.200 | 192.168.1.200 | Success | Connected routes in both directions
2 | 192.168.1.100 | 192.168.3.100 | Success after routes | Static route forward and return paths
2 | 192.168.1.200 | 192.168.3.200 | Success after routes | Same routed networks as above
2 | 192.168.1.100 | 192.168.1.200 | Success | Same LAN / subnet
First ping can occasionally time out while ARP tables are populated. Repeat the ping and inspect the event list before diagnosing a fault.
Computer and Network Communications | Static Routing & ICMP Ping 10

## Slide 11
10. Troubleshooting Checklist
Symptom | Likely cause | What to check
Cannot ping own gateway | Wrong PC IP/mask, cable, or interface down | PC IP Configuration; link lights; show ip interface brief
Local LAN works, remote LAN fails | Missing or incorrect static route | show ip route; verify destination network, mask, next hop
Request arrives but no reply | Return route or wrong gateway missing | Check route on the remote router and destination PC gateway
Interface is administratively down | no shutdown not applied | Enter interface configuration and issue no shutdown
Wrong subnet mask | Hosts disagree about local vs remote network | Use consistent masks for all devices in each LAN/link
Duplicate IP address | Two devices share an address | Ensure every interface and PC has a unique IP
Computer and Network Communications | Static Routing & ICMP Ping 11

## Slide 12
11. Analysis and Discussion
• Topology 1 demonstrates inter-LAN communication through one router. Since both networks are directly connected, the router installs connected routes automatically when interfaces are up.
• Topology 2 demonstrates routing between remote LANs. Static routes tell each router where to send packets for networks that are not directly connected.
• A successful ping confirms two-way reachability for ICMP at that time; it does not prove every application or protocol will work.
• The first ping may take longer because ARP must discover the next-hop or destination MAC address.
• In routed traffic, routers replace the Layer 2 Ethernet header on each hop, while end-to-end IPv4 source and destination addresses normally stay unchanged.
• Simulation Mode makes the forwarding sequence visible and helps connect routing-table decisions to observed packet events.
Computer and Network Communications | Static Routing & ICMP Ping 12

## Slide 13
12. Conclusion
Key findings
• Ping uses ICMP Echo Request and Echo Reply to test IP reachability.
• Correct IP addresses, subnet masks, gateways, and active interfaces are essential.
• A single router can route between its directly connected LANs without static routes.
• Two routers require appropriate routes to remote LANs and a valid return path.
• Packet Tracer Simulation Mode shows how ARP, ICMP, and router forwarding work together.
Before submission: attach screenshots of successful pings and the Simulation event list from your own Packet Tracer project.
Computer and Network Communications | Static Routing & ICMP Ping 13

## Slide 14
Appendix — Commands and Submission Evidence
Useful verification commands
show ip interface brief
show ip route
show running-config
ping 192.168.3.100
tracert 192.168.3.100
Recommended evidence
• Full topology screenshot with device labels visible.
• PC IP Configuration for representative hosts.
• Router interface status and routing table.
• Successful ping output for local and remote hosts.
• Simulation Mode event list for one end-to-end ping.
Addressing note: the slide tables transcribe the visible IP labels. Confirm the actual interface names and masks in your Packet Tracer file before submitting.
Computer and Network Communications | Static Routing & ICMP Ping 14